## Slide 1: Value Stream Mapping
By Ethan bolander, peter Schulte, and Dominique western
Select “Slide Show” or this speaker icon to begin the narrative presentation!
Notes: Hello and welcome! This is a tutorial on value stream mapping and how to make one! Where seeking the untapped potential of operations of mature business would otherwise be assumed to be optimal, value stream mapping provides a visual understanding of the overall current process involved in a facility or production line whether it’s supplying customers with product(s) or simply making toast, it has the capability (given enough imagination and creativity) to create a future state map. As with all of lean manufacturing, value stream mapping –which is a part of lean manufacturing- demands attention. In value stream mapping in particular, data and process comprehension are required in order to successfully complete a value stream map. To complete a value stream map an understanding of information flow, material flow, and identifying and measuring the timing of these processes is needed. So let’s begin!

## Slide 2: Instructions - Two Ways to Learn
Main function
This Power Point is designed for you to go through each slide listening to the narration. Each slide will automatically transition to next.
Alternate function
You can click on icons in the next slide, which is a complete Value Stream Map (VSM), to take you to the description of that icon.
From there, you can either go to the icon glossary by clicking on the icon in the icon info or go back to the complete VSM by clicking on the button below.
Return to VSM
Notes: The main function of this presentation is to be run in “presentation mode” to allow a narrative to guide you through how to make a value stream map. Alternatively, it can be run through manually by leaving it in the “viewing” or “editing” modes. Feel free to click on the “Return to VSM” button if you would like to see the main example we will be using for this presentation at any time during this presentation.

## Slide 3
Source: http://en.wikipedia.org/wiki/Value_stream_mapping
Notes: Provided is an example of a value stream map. By the end of this technical description you should be able to complete this as well as many other kinds of value stream maps. To begin, let’s start where every business does: with the customer and, in general, with the flow of information known as the “Information Flow” section of a value stream map.
This is the value stream map we will be using as our example for the presentation. If you mouse over any of the icons you’ll find that you can click on any of them, which will jump you to the segment that introduces them. Otherwise, sit back and relax as we show you how to write a value stream map.

## Slide 4: Information Flow Section
Notes: We first start with the “Information Flow Section” of a value stream map, which pertains to all data and information that flows in order for a purchase order to be placed and that we may order the supplies and provide our consumer with their desired product!

## Slide 5: Customer and Supplier
Icon Info
The “Outside Sources” icon is used to show customer and suppliers.
Return to VSM
Notes: Let’s start by making our symbol for a customer. This can be recognized as a rectangle with right triangles facing the same direction on top of the rectangle, and the name of the outside source affiliated with this part of the process, whom we will simply call, “Customer”. As you can see in our diagram, you’ll want to place this icon in the top right corner of the map.

## Slide 6: Electronic Information Flow and Production Company
Icon Info
Represents the process within your company that will make the product.
Icon Info
Represents data that is transferred electronically.
Return to VSM
Notes: Our next step is to connect this outside process to our own company, or more specifically to the “Production control” process of our company for this example which is recognized by a rectangle with a top section of it for titling the process. Since this is a flow of data we’ll need to recognize whether it is an electronic data flow, such as an email, online order, or faxed order, or manual data flow such as a mailed or hand-delivered order. These two can be distinguished by either a black lightning bolt for electronic, or a straight black line for manual. In this example we’ll be using only black lightning bolts as shown. As you can see, it’s also helpful to show any other helpful information such as order frequency on the information flow lines.

## Slide 7: Time Period Information
Icon Info
Describes the time period of information flow.
Return to VSM
Notes: When the order comes back to our process, we then have to send on an order for supplies up the order chain to our suppliers in order to receive our materials so that we can produce the product our customers are ordering for. For this part, we’ll simply repeat what our customer did to us as we do to our suppliers but on a different frequency of re-ordering. In more complex operations you’ll find information flowing from inside the company to various processes that also interact with multiple points in the material flow section which you can see in one of our more complex examples at the end of this presentation.

## Slide 8: Material Flow Section
Notes: So after we’ve order our supplies from our supplier, we move into the material flow section as we receive our parts.

## Slide 9: Movement of goods
Icon Info
Shows movement of finished goods to customer.
Return to VSM
Notes: To show the material movement, we make a solid arrowhead-bar that will go from the supplier to our first in-company process. This arrowhead-bar represents the movement of finished goods. In this case, the product is considered a “finished good” as it comes from the supplier, but when the supplies get to our facility they will become “unfinished goods”. We’ll refer to the unfinished goods as production materials which you will see in a moment.

## Slide 10: Shipping Truck
Icon Info
Note frequency of shipments.
Return to VSM
Notes: In material moving from inside/outside our example facility, we’ll be including a truck icon to represent a shipment coming in to drop the material off as well.

## Slide 11: Manufacturing Process
Icon Info
One process box represents a single area of operation
Return to VSM
Notes: To represent our first process, we create a process box, just as we made one for the “Production control” box.

## Slide 12: Operator
Icon Info
Represents a person.
Return to VSM
Notes: In order for anything to be done, we’ll need operators! So here we show a symbol that represents an operator that is in “Process A”, but only one operator. To show more than one, simply create multiple icons of the operator icon or put a “x#” for the number of operators in the process.

## Slide 13: Data Box
Icon Info
Used to record information concerning a manufacturing process.
Return to VSM
Notes: In each process moving forward we’ll also add other relevant information below the process box so that viewers of this value stream map will be able to see information such as cycle time, takt time, uptime, number of shifts, and time running. This section can include more or less information than this as you find information relevant or not depending on the processes being done.

## Slide 14: Inventory
Icon Info
Shows inventory segment. Count should be included.
Return to VSM
Notes: As we move forward we will place a yellow triangle between our “Process A” and what will be “Process B” which represents an inventory section, or what it’s better recognized as: a stopping point for material as it waits for the next process. Production material waiting in inventory from one process to the next is very common whether it’s for a few minutes or a few days. The inventory symbol also usually has associated with it a number which is to show the count of production material parts in the inventory as it waits for the next process to take it for further work to be done in order to turn the product more and more into what our customer ordered. In this step you’ll also see that we switched to the production material icon moving via a striped arrowhead-bar to represent the production material which is no longer considered “finished material”.

## Slide 15: Movement of Production Material
Icon Info
Shows the physical movement of unfinished product.
Return to VSM
Notes: And here’s the production material icon defined. In following the process used to get this far in the material flow section, we’ll repeat it for completing the rest of the material flow section which will end with the material leaving our final process and returning back to the customer as finished product.

## Slide 16: Lead Time Section
Notes: But that’s not all! One of the most valuable things about the value stream map besides the visual representation of how a part or parts move through you facility, is the lead time section that tells us how much time is spent on average in each process. Warning: time studies may be required to fill out this section!

## Slide 17: Process Time
Icon Info
Shows the time Process A takes to complete one part/batch/assembly
Return to VSM
Notes: The times for this are separated vertically into two levels: one for processes, and one specifically for inventory.

## Slide 18: Production Lead Time
Icon Info
Shows the travel time/ waiting time for parts ready for next process.
Return to VSM
Notes: These times can be different time units from each other, but should be the same between process times, and the same between inventory times. Also note that only a single connected line goes from the beginning of the lead time ladder to the end where each section of time shown is directly below the process or inventory section that it is capturing the time of.

## Slide 19: Total Production and Process Time
Icon Info
Total production lead time and processing time.
Return to VSM
Notes: After completing this portion of the lead time ladder, the times are totaled up at the end to show total time in processing and total time in inventory which completes our value stream map. Congratulations!
After you’ve given yourself a pat on the back, let’s continue on to some of our extra examples to show more extensive uses of value stream mapping.

## Slide 20: Further Information
VSM Profits
http://asq.org/learn-about-quality/lean/overview/value-stream-mapping.html
Program to Create a VSM
https://support.office.com/en-ie/article/Create-a-value-stream-map-35a09801-999e-4beb-ad4a-3235b3f0eaa3
Book on VSM
“Value Stream Mapping: How to Visualize Work and Align Leadership for Organizational Transformation” (2013) by Karen Martin and Mike Osterling
Notes: If you feel inclined to learn more about value stream mapping, please click on either of the two hyperlinks shown or search for this book online or at your local book store.

## Slide 21: End of Slide Show – Icon Glossary
Attention: Boxes outlined in Red are icons that may be used in the examples and in real situations, but will not take you anywhere in the power point.
Notes: Thank you for joining us for this presentation and we hope you learned a lot about value stream mapping! In a few moments you’ll be directed on to our icon glossary where you can learn about all the different icons we used and didn’t use in our presentation that can be implemented in value stream mapping!

## Slide 22
Information Icons | Represents | Notes
 | Electronic information flow | Data that is transferred electronically.
 | Information | Describes the time period of information flow.
 | Manual Information flow | Shows production and shipping schedule
 | Load Leveling | A tool to intercept batches of Kanban and level of volume and mix of them over a period of time.
 | Sequenced-Pull Ball | A pull system to make subassembly processes without a supermarket in a way that gives instructions on a predetermined type and quantity.
 | “Go See” Production Scheduling | Buffer or safety stock must be noted.
 | Production Kanban | The “one-per-container” Kanban. It is a card or device that tells how many of what can be produced.
 | Withdrawal Kanban | A card or device that tells the material handler to get and transfer parts.
 | Signal Kanban | The “one-per-batch” Kanban that tells when a reorder point has been reached and another batch needs to be produced.
 | Kanban Post | A place where Kanban are held and collected.
 | Kanban Arriving in Batches | 
Attention: Boxes outlined in Red are icons that may be used in the examples and in real situations, but will not take you anywhere in the power point.
Return to VSM Example

## Slide 23
Material Icons | Represents | Notes
 | Outside Sources | Used to show customers and suppliers.
 | Manufacturing Process | One process box represents a single area of operation
 | Data Box | Used to record information concerning a manufacturing process.
 | Inventory | Count should be included.
 | Truck Shipment | Note frequency of shipments.
 | Movement of production material | Is material that is moved forward after being produced and it happens before the next process needs it.
 | Movement of finished goods | Shows movement of finished goods to customer.
 | Supermarket | A controlled inventory of parts that is used to schedule production at an upstream process.
 | Withdrawal | Pull of material, usually from a supermarket.
Attention: Boxes outlined in Red are icons that may be used in the examples and in real situations, but will not take you anywhere in the power point.
Return to VSM Example

## Slide 24
General Icons | Represents | Notes
 | Buffer or Safety Stock | Buffer or safety stock must be noted.
 | Operator | Represents a person.
Attention: Boxes outlined in Red are icons that may be used in the examples and in real situations, but will not take you anywhere in the power point.
Return to VSM Example