## Slide 1
Designing Flexible Electric Generation Portfolios in Iowa
Xue Lei
Cameron MacKenzie
Kyung (Jo) Min
Ramin Giahi
Industrial and Manufacturing Systems Engineering,
Iowa State University, Ames, Iowa.

## Slide 2: Introduction
Iowa Electric Profile (2020 - Including Non-Utility Generation)
ELECTRIC GENERATION IN IOWA BY PRIMARY ENERGY SOURCE | 2020 NAMEPLATE CAPACITY (MW) | PERCENT OF NAMEPLATE CAPACITY | 2020 GENERATION (MWH) | PERCENT OF GENERATION
Coal | 5,754.7 | 25.61% | 14,146,835 | 23.72%
Wind | 11,406.9 | 50.76% | 34,182,302 | 57.32%
Nuclear | 0.0 | 0.0% | 2,904,863 | 4.87%
Natural Gas | 4,215.0 | 18.76% | 7,036,824 | 11.80%
Hydro | 129.2 | 0.58% | 1,025,215 | 1.72%
Other & Other Renewables | 22.0 | 0.10% | 207,440 | 0.35%
Petroleum | 924.2 | 4.11% | 111,111 | 0.19%
Solar | 18.4 | 0.08% | 22,082 | 0.04%
Total | 22,470.4 | 100.00% | 59,636,672 | 100.00%
https://iub.iowa.gov/iowas-electric-profile
2

## Slide 3: Introduction
Challenges in planning for the future:
  Uncertainties
    Demand
    Costs (investment, fuel)
    Requirements for using renewable sources
    Future carbon emission limit
  Need to make decisions at different stages
Flexible electric generation portfolio will provide a more reliable planning for the future
3

## Slide 4: Problem description
Decision variables: Choose capacity for each electricity technology at each stage
Objective: Minimize total cost
  Investment
  Operations and maintenance
  Cost of fuel generation
  Salvage value
Constraints
  Capacity greater than demand
  Power flow equations
  Requirement that X% comes from renewable resources
  Limit on carbon emissions
  Limit on natural gas
Uncertainties
D. Mejia-Giraldo and J. D. McCalley, “Maximizing future flexibility in electric generation portfolios,” IEEE Transactions on Power Systems, vol. 29, no. 1, pp. 279–288, 2014.
4

## Slide 5: Related research
Electric generation planning with uncertainty Stochastic programming
  Two-stage stochastic optimization
  Multi-stage stochastic optimization
  Large number of uncertain scenarios: scenario reduction methods
Limitations:
  The number of required scenarios needs to be decided
  The selected scenarios might ignore the valuable information from eliminated scenarios.
5

## Slide 6: Methodology
Deep reinforcement learning
  Provide the optimal generation planning for each simulated uncertain scenario using a learned neural network
  The neural network is trained by the action and reward pairs
Myopic planning
  Decision making that focuses on optimizing for the current period
  Combine the Monte Carlo simulation with myopic planning to generate long-term planning for electric generation.
6

## Slide 7: Deep-learning methodology
R. Giahi, 2020. “Sequential decision making and simulation-optimization for the design of complex engineering systems.” PhD Dissertation, Iowa State University. https://lib.dr.iastate.edu/etd/18317/
7

## Slide 8: Application
Planning horizon = 10 years = 5 periods
Each period consists of 3 demand profiles
Uncertainties:
  investment in wind power
  demand for each time period
  renewable power source percentage
  carbon emission limit
For each uncertain parameter, 2 potential change rates are considered
Assume that the fuel-based technology using coal and natural gas will need to retire in the next 10 years
8

## Slide 9: Alternatives for electricity generation
9

## Slide 10: Myopic planning results for the state of Iowa
10

## Slide 11: Preliminary conclusions
Wind energy is most cost-effective solution in Iowa for new generation sources
Neural network in deep reinforcement learning (PyTorch)
  Did not produce accurate results in a reasonable amount of time
  Potential fixes
    Adjust parameters in neutral network
    Additional GPUs
    Adjust algorithm to sample more intelligently
11

## Slide 12: Future work
More research needs understand the conditions when reinforcement learning provides more accurate results than myopic planning
Include additional energy sources such as solar power and petroleum
Additional complexity (e.g., time to install new generation)
Additional constraints to reflect policy goals for renewable resources
Acknowledgements
  Iowa Energy Center (Solar and Wind Energy using Engineering Economics Theory, SWEEET, https://www.imse.iastate.edu/sweeet )
  Diego Mejia-Giraldo for providing data file from his original study
12

## Slide 13
Q&A
Xue Lei, xlei@iastate.edu