## Slide 1
Optimal Valuation of Project Options in Electric Power Generation and Transmission Planning
Cameron MacKenzie
Gazi Nazia Nur
Jay Sandeep Ghodke
Kyung Jo Min
Industrial and Manufacturing Systems Engineering
Iowa State University

## Slide 2: How should we value new renewable energy resources?

## Slide 3: Electricity prices can be very volatile and uncertain

## Slide 4: Solar and Wind Energy Using Engineering Economics Theory (SWEEET)
www.imse.iastate.edu/sweeet

## Slide 5: Optimal power flow model determines best operating levels for electric power generation
Objective: Minimize cost while meeting demand

## Slide 6: Real options give firms the right but not the obligation to undertake business opportunities
Timing / waiting option
Growth
option
Abandon / switch / install option

## Slide 7: Adding new generation sources or transmission capacity is a critical part of power planning
7

## Slide 8: 3-bus network: Bus 1 has no generator and the demand will be satisfied by generators 2 and 3
8
What is the value of adding a generator at bus 1?
What is the value of adding another transmission line from bus 2 to bus 1?
Load
Generation cost
Transmission capacity

## Slide 9: Demand at bus 1 follows geometric Brownian motion and can increase or decrease in each period (lattice)
Initial demand = 200 MW
Volatility = 30% per year
Risk-free discount rate = 5% annual
Time horizon = 5 periods
Up value = 1.35
Down value = 0.741
Risk-neutral probabilities
Probability of up = 0.51
Probability of down = 0.49

## Slide 10: If a new generation unit at bus 1 costs $100,000 with a generation cost of $7.92 per MWh, the real option value is $620,000
Hold
Hold
Add
Millions of $

## Slide 11: Option value increases with modelling horizon

## Slide 12: Option value is non-monotonic with respect to volatility

## Slide 13: If a new transmission line with capacity of 105 MW from bus 2 to bus 1 costs $100,000, the real option value is $1.01 M
13
Hold
Hold
Add
Millions of $

## Slide 14: Why is the option value for transmission more than the value for generation?
Load
Generation cost
Transmission capacity
105MW
Optimal power flow calculations  location marginal price
14

## Slide 15: Real option value model assumes cost uncertainty can be hedged
What if cost uncertainty cannot be hedged or only partially hedged?
Loss to initial position
Gain to hedge
Neutral exposure or reduced risk

## Slide 16: Value of option for new generation unit with no hedging
Install generation immediately
Install generation in period 1 if demand increases
Wait until period 2

## Slide 17: Value of option for new generation unit with partial hedging
Value of option (in $ million)

## Slide 18: Real option theory with optimal power flow model can value new generation and transmission capability
$620,000 for new generation unit
$1.01M for new transmission line
Excel spreadsheets to enter your own calculations
www.imse.iastate.edu/sweeet

## Slide 19
Q&A
Cameron MacKenzie, camacken@iastate.edu,
www.imse.iastate.edu/sweeet